## Slide 1: Simulation and Analysis of Inter-satellite Communication for Real-Time Data Downloading
Student Name: Tsang Chun Hei
Student ID: 21032048d
Supervisor: Dr. LYU Mingsong

## Slide 2: 1. Problem
The limitation of traditional Satellite data transmit

## Slide 3: 4,700
Active Low Earth Orbit (LEO) Satellites till to 1 May 2022

## Slide 4: Low Earth Orbit (LEO) Satellites
Below 2000 kilometers above the earth
Lower signal propagation delay in LEO
Efficiency communicate with Earth-based stations
Capture more detailed pictures

## Slide 5: LEO Satellite used to
Communications
Observe Ground
Military Reconnaissance
Navigation
…

## Slide 6: However….
LEO Satellite Coverage issues
Limited Ground Station
May not be able to transmit data to the ground immediately
May need to wait until reach the communication scope of Ground Station

## Slide 7: Experiment result
Transmit to the Ground Station
  Nearby  More than 10 seconds
  opposite on earth  Around 3050 seconds
  Far away to the orbit  more than 3050 seconds
It is not able to meet the real-time system constraints

## Slide 8: 2. Solution
How to solve the limitation

## Slide 9: To Solve the Problem
Inter-satellite communication
  Transfer data from Satellite to Satellite
  Reach the Satellite in the target communication scope
Finally transfer to the target Ground Station

## Slide 10: Difficulty
LEO Satellite and Ground Station positions are not constant
  Calculate the Earth-centered inertial(ECI) position with the time dimension
How to decide which satellite transfer to
  Design and use Path Decision Algorithm

## Slide 11: 3. Simulator
A simulator to proof and implement the solution

## Slide 12: Objective
Given a Set of LEO Satellite, a target Ground Station, and an Observation Point
Simulate the behavior of
  LEO Satellite and Ground Station position change
  the Communication
Calculate the data transmit path and delay

## Slide 13: Introduction
Use Earth-Centered Inertial (ECI)
  3-dimensional Cartesian coordinate system
  Original fixed center in the Earth's mass center
  Fixed with respect to the stars
  Position on Earth is always changed by the Earth’s rotation

## Slide 14: Components Flowchart
Visibility Model
Path Decision Model
Communication Delay Model

## Slide 15: Path decision Algoirthm
A*
Dijkstra
Orbit Base

## Slide 16: A*
Update the time after decided the next node
Less iteration
Great performance

## Slide 17: Dijkstra
Update the time after decided the whole path
Most iteration
Best performance

## Slide 18: Orbit Base
Update the time after decided the next node
Less iteration
Normal performance

## Slide 19: Parameter of the Simulator
Inclination
Define the inclination angle of the LEO Orbit.
Default Value: 97 degree
Argument of Perigee
Define the inclination angle of the LEO Orbit.
Default Value: 0 degree
Motion
Define the orbit revolution around earth per day.
Default Value: 14
Orbit Size
Define the numbers of orbit.
Default Value: 9
Satellite Size
Define the numbers of Satellite for each orbit.
Default Value: 25
Off Nadir
Define the off-nadir angle of LEO Satellite to observation.
Default Value: 45 degree

## Slide 20: Parameter of the Simulator
Buffer Delay
Define the buffer delay from network congestion to each Satellite. Default Value: 0.05 seconds
Process Delay
Define the process delay from processing data on Satellite.
Default Value: 0.01 seconds
Package Size
Define the package size of data to transmit.
Default Value: 56623104 Bytes (54MB)
Data Rate
Define the data rate of the Satellite signal for data transmit.
Default Value: 530579456 Bytes/s (506MB/s)
Signal Speed
Define the signal speed of the Satellite to transmit data.
Default Value: 299792458 m/s

## Slide 21: Experiment result
 | A* | Dijkstra | Orbit Path
Mean Time to the opposite on Earth | 0.74 | 0.7395 | 0.826
Mean time to Longitude change location | 0.478 | 0.475 | 0.6453
Mean time to Latitude change location | 0.415 | 0.411667 | 0.41533

## Slide 22: 4. Demo
Demo of the Simulator

## Slide 24: Thanks!
Any questions?
You can find me at 21032048d@connect.polyu.hk